IMPLEMENTATION OF REGULATORY FRAMEWORK

TASK IDENTIFICATION FORM

| DATE ORIGINATED: | July 13, 2004 | DATE REVISED: | January 10, 2006 |
| --- | --- | --- | --- |
| WORKING GROUP: | Network (NT) |
| TASK #: | 14 | FILE: | NTTF014M.doc |
| TASK TITLE: | IP Interconnection Profile for interconnection between service providers under the jurisdiction of the CRTC. |
| TASK DESCRIPTION: | To develop an IP-to-IP interconnection interface guideline initially for Telephony service providers under the jurisdiction of the CRTC. |
| CRTICAL TASK: | N |
| PRIORITY: | M | DUE DATE: | September, 2005 |
| CROSS IMPACTS: |  |
| WORK PLAN AND TIME FRAMES: | To develop an IP-to-IP interconnection interface guideline that will consider the following: Interconnection between Telephony service providers under the jurisdiction of the CRTC. The functionalities of the approved CCS7 minimum message set. Service functionalities to be supported and the information that needs to be exchanged across the network-to-network interface. IP standards and protocols that are commonly used for carrier-to-carrier interconnections. The initial focus will be on the Session Initiation Protocol, but other protocols will not be excluded. Carrier specific implementation requirements will not be considered in this TIF. Relevant standards-developing bodies and current IP standards development processes within these standard bodies. February 2005: A list of feature and corresponding message sets in IP based on the approved TIRE009 (SS7 minimum message set) April 2005: Document standards / protocols and standard developing and accreditation bodies June 2005: Draft report |
| CURRENT STATUS: | In Progress |
| TASK SPONSOR: | Henry Yabar, P. Eng. MTS Allstream Inc. 200 Wellington Street West Toronto, Ontario M5V 3G2 TEL: 416-644-9645 FAX: 416-644-9724 [Mailto:henry.yabar@allstream.com] |
| TASK TEAM: | Members of the Network Working Group |

ACTIVITY DIARY:

|  | Date | Activity |
| --- | --- | --- |
| 01 | 9Nov04 | The NTWG Chair reported that the Steering Committee would like to see a more detailed TIF work plan. This work plan was developed and is now included in the “Work Plan and Time Frame” section of this TIF report (page 1). |
| 02 | 9Nov04 | It was agreed to add the background information to the TIF to make it self-contained. The background information would include the contributions and minutes of the discussions prior to the approval of the TIF. |
| 03 | 9Nov04 | The NTWG Chair reiterated that the TIF should focus on the technical interface and that policy issues should not be discussed. Gray issues should be identified but not discussed. H. Charles stated that only high-level service requirements should be discussed. After a brief discussion in which several parties intervened, it was agreed that IP application layer standards & protocols should be the focus of the TIF while architectural and non-application layer issues should not be discussed. |
| 04 | 9Nov04 | Due to the increased number of participants now attending CISC NTWG that missed discussing the “Work Plan and Time Frame” section, Henry Yabar, the task sponsor reviewed each of the five items contained in this section. Interconnection between Telephony service providers under the jurisdiction of the CRTC. - Accepted without comments. The functionalities of the approved CCS7 minimum message set. - At least one person asked for clarification. - Several parties responded that the starting point of the task is to identify in the IP interface the minimum message set equivalent to the one specified in the report TIRE009 (available on CRTC Web site). - It was also stated that the required network interface should allow the interchange of the messages of a service offering, for example Follow-me service, if both service providers offer the same service to their customers. Service functionalities to be supported and the information that needs to be exchanged across the network-to-network interface. - Several parties suggested the identification of additional features and the method to handle these additional features would be included. - TELUS stated that the principle already exists in dealing with exchanging messages for optional features. Namely, if optional features are offered by interconnecting service providers, the message associated with those features will be exchanged between the service providers by mutual agreement. IP standards and protocols that are commonly used for carrier-to-carrier interconnections. The initial focus will be on the Session Initiation Protocol, but other protocols will not be excluded. Carrier specific implementation requirements will not be considered in this TIF. - Videotron (VTL) asked what protocols will be supported and what protocols are available and implemented in the industry e.g., SIP, H.323? VTL proposed an industry scan of preferred protocols. - Bell Canada stated that an industry scan is not required but contributions from the participants would be a more efficient way to identify relevant protocols. - VTL stated that the basic interconnection requirements in the IP world are security, performance and quality of service. Before protocols are considered, basic IP interconnection issues like security, number of links for signaling and data types should be investigated. Are we going to consider functionality first and security second; are basic IP interconnections going to be considered, are carriers allowed bi-lateral arrangements? - Several parties responded that these are valid concerns and could be investigated depending on the policy aspect of the investigation but they were out of scope for this TTIF since this TIF is only looking at application layer protocols. Additionally, it was suggested that these issues be placed into a parking lot so as to not lose the thought. - Louis Lepage (Commission staff) suggested that session border controllers can be used to provide control between autonomous systems. - Bell suggested we consider vendor seminars for IP issues and requested that each participant make a conscious effort to bring vendors to talk about a list of topics. -The NTWG Chair expressed that the primary objective of CISC NTWG is to resolve industry issues and not to provide technical training. To the extent that vendor seminars are required to help understand and resolve an industry issue, the seminars would be welcome. MTS-Allstream and several parties concurred and expressed that presentations are recognized to be very useful to illustrate specific alternatives in a technical discussion. - Microcell asked if a LEC could refuse an IP interconnection to another LEC. Louis Lepage (Commission staff) stated, yes they could. However, this will probably change when IP arrangements become prevalent. - H. Charles requested clarification on whether financial institutions were considered to be under CRTC jurisdiction. Louis Lepage answered: No, only carriers and resellers of carrier services. - VTL asked if IP to IP interconnection is mandated. Louis Lepage answered: No, not at this time because of the implication with Internet backbone issues. - VTL expressed that care should be taken in considering IETF standards because of the ‘best effort’ nature of the internet. VTL also expressed that SIP is emerging as the favored protocol at this time but because of the fluidity of the Internet and its’ standards, SIP may be obsolete sooner than we would expect. - Several parties suggested that since the NTWG is not selecting an interconnection protocol that must be used for IP interconnection but rather, establishing principles of what each protocol must provide (i.e., minimum message set, etc.), that our efforts fit very well with the fluid nature of the Internet. - H. Charles proposed that consideration b e given to the need for the transport of 911 calls between IP networks. Relevant standards-developing bodies and current IP standards development processes within these standard bodies. It was agreed to include the standards developing bodies together with the standards accreditation bodies. It was also agreed that “Standard” as defined in this TIF would also include industry guidelines - Several parties mentioned the industry bodies to consider include ITU, ATIS, IETF, IEEE, ISO, etc. - K. Richardson noted the difference between standards developing bodies and standards accreditation bodies. |
| 05 | 9Nov04 | After a brief discussion, the following time table was agreed to complete the activities listed: - Item 1 Feb 2005 - Item 2 Feb 2005 - Item 3 Feb 2005 - Item 4 April 2005 - Item 5 April 2005 - Report 1st draft June 2005 |
| 06 | 07Dec04 | The TIF was reviewed and approved as amended. |
| 07 | 07Dec04 | Clear Cable Networks stated that we can not preclude internet protocols based on the public Internet when we may be using those protocols on the private internet. |
| 08 | 15Feb05 | The TIF was reviewed and approved as amended. |
| 09 | 15Feb05 | Mark Seagal from FCI Broadband commented that the CRTC tracks BGP border gateway protocol for peer-to-peer interconnections. The Chair to ask the CRTC staff about this issue. |
| 10 | 15Feb05 | XIT Telecom presented its contribution NTCO301. Mark Seagal stated that CRTC does not object bi-lateral interconnection agreements. Allstream stated that if ILECs offer a service for themselves or to another party (bilateral agreement), they have to make it available to any one who requests it from them.H. Charles stated that the purpose of the TIF is NNI meeting the needs of the Minimum Message set and that Xit Telecom’s contribution does not address this issue. Allstream agreed, as well as Xit. D. Kwong stated that SIP Connect is a vendor spec not a standard spec. SIP Connect is a UNI spec, not a NNI spec. There is a draft document in the industry which addresses NNI: PTSC-SAC-2005-005R1 (ATIS based document). |
| 11 | 15Feb05 | The Chair requested a revised work plan for the next meeting. H. Yabar to present the revised work plan. |
| 12 | 15Mar05 | The TIF was reviewed and approved as amended. |
| 13 | 15Mar05 | Henry Yabar, per the Chair’s request to present a revised work plan, and given that the work plan was approved by the NTWG, tabled the following revised time frames proposal: To develop an IP-to-IP interconnection interface guideline that will consider the following: 1. Interconnection between Telephony service providers under the jurisdiction of the CRTC. 2. The functionalities of the approved CCS7 minimum message set. 3. Service functionalities to be supported and the information that needs to be exchanged across the network-to-network interface. 4. IP standards and protocols that are commonly used for carrier-to-carrier interconnections. The initial focus will be on the Session Initiation Protocol, but other protocols will not be excluded. Carrier specific implementation requirements will not be considered in this TIF. 5. Relevant standards-developing bodies and current IP standards development processes within these standard bodies. (February 2005) May 2005: A list of feature and corresponding message sets in IP based on the approved TIRE009 (SS7 minimum message set) (April 2005) July 2005: Document standards / protocols and standard developing and accreditation bodies (June 2005) September 2005: Draft report |
| 14 | 15Mar05 | In response to Allstream’s statement “if ILECs offer a service for themselves or to another party (bilateral agreement), they have to make it available to any one who requests it from them.”; TELUS notes that Allstream has over-generalized Section 27 (“Unjust Discrimination”) of the Telecommunication Act indiscriminately. TELUS also notes that a “bi-lateral agreement” needs not be available to all those who request it so long as it does not contravene the Telecommunication Act. |
| 15 | 15Mar05 | Due to the unavailability of the contributor to present NTCO302, the late arrival of other contribution and the short time available for the presentation of NTCO304, it was agreed to postpone the presentation and discussion of these contributions for the next April 18-19, 2005 meeting. |
| 16 | 19Apr05 | The TIF was reviewed and approved as amended. |
| 17 | 19Apr05 | H. Charles presented NTCO302. H. Charles proposed to review and to accommodate any new requirements that would be necessary (ENUM, 911, etc). This would allow the guidelines to encompass everything required. K. Richardson stated that 6 months ago it was agreed to the task. What is IP minimum message set. We decided deliberately to avoid discussing some issues which now H. Charles suggests to add. Bell Canada opposed to the suggestion of testing IP to IP at his time; not NNI only. Interoperability is key in terms of vendor equipment. Xit expressed its agreement with section 3. in NTCO302. The Chair expressed that SIP Connect is a subset of the Minimum Message Set. Does the NTWG want to accept a reduction of the Minimum Message Set? Xit stated: What is the mapping TDM to IP? With that we would understand CCS7 and then we will analyze its implementation in IP, and then we can decide whether we covered all or a subset of the Minimum Message Set. H. Charles expressed that it is essential That NTWG determines the level of detail required to be interchanged H. Charles proposes to take into account other activities taking place in the industry, as ESWG, HPC, ENUM, etc. H. Charles stated that security is not as significant an issue in the TDM environment as it is for IP inter-networking. Xit, related to section 4 and 5 in NTCO302, asked if 710 would need to be considered. Cogeco (Dennis Chartier) expressed that simple specs (first building block of a call), SLA, QoS, et. Industry Canada (Louis LePage) expressed that the TIF was purposely defined as it is. |
| 18 | 19Apr05 | TELUS (R. Sired) presented NTCO304. R. McCann asked if two SIP end points can set-up a call without a proxy server. K. Richardson asked how do we relate this to NTTF014. In response, Sam Yung (Chair) stated that the work plan requires the Working Group that “To develop an IP-to-IP interconnection interface guideline that will consider the following: … 4. IP standards and protocols that are commonly used for carrier-to-carrier interconnections. The initial focus will be on the Session Initiation Protocol, but other protocols will not be excluded. Carrier specific implementation requirements will not be considered in this TIF.” TELUS’ contribution provided a scan of the IP protocols that exist in the industry for interconnection. In fact, it is the only contribution so far that supports the work plan item #4. Regardless of what the final recommendation would be, the Working Group would not have exercised due diligence that was expected of it without such industry scan. R. McCann asked for a summary of the protocols in use by VoIP providers are using today R. Sired clarified that TELUS position is to support multiple protocols |
| 19 | 19Apr05 | Bell Canada (D. Kwong) presented NTCO305. D. Kwong stated that SIP Connect is a UNI. Deriving an NNI from a UNI is not recommendable, specially if it is Manufacturer’s based specs. K. Richardson stated that ATIS documentation is only freely available to ATIS members. D. Kwong provided the following url: http://contribution.atis.org/upload/PTSC/SAC/ptsc-sac-2005-074R1.doc K. Richardson stated that the documentation is not generally available. |
| 20 | 19Apr05 | F. Menard presented NTCO306. The Chair asked if it was Xit Telecom intention that the NTWG develop the s/w for the SIP stack. F. Menard answered no S. Yung asked if different tools provide the same SIP stack. F. Menard answered No F. Menard stated that software engineering modelization of protocols is complemented with FDL. The result is to be able to show in a graphic manner the protocol that is being discussed. Ind. Canada (Louis LePage) stated that even a perfect stack needs to address interoperability because of the underlying protocols, permissible delays, etc. D. Kwong asked what is the background of EventHelix.com F. Menard replied that it is a s/w vendor. Regarding the security of the signalling system, D. Kwong stated that SS7 is not an open system. It is a closed system. D. Kwong also expressed that the architecture suggested for ENUM by Xit had not been adopted. |
| 21 | 19Apr05 | K. Richardson presented NTCO307. S. Yung commented that the contribution seemed to present the idea of doing all the work only on SIP and exclude other protocols. Sam made his objection clear. K. Richardson stated that his contribution does not exclude other protocols. CallNet (P. Lang) stated that from the practical point of view, we may end up discussing only SIP. |
| 22 | 19Apr05 | K. Richardson presented NTCO308 K. Richardson asked if we could ask the Commission for help in accessing to the PTSC-SAC document and the ability to participate in the making of this document |
| 23 | 19Apr05 | Cogeco (D. Chartier) asked a question on process: From three deliverables, can we deliver only one? H. Yabar stated that we are committed to deliver all three. |
| 24 | 19Apr05 | The Chair invited the ILECs to document the CCS7 messages flow. The Chair also invited to all parties to make contributions to document the Minimum Message CCS7 ISUP messages flow in a single document. F. Menard indicated that TCAP messages might need to be included as well. D. Kwong clarified that some TCAP requirements relate to wholesale services which are not included in the Minimum Message set. |
| 25 | 17May05 | The TIF was reviewed and approved as amended. |
| 26 | 17May05 | K. Richardson stated that SIPConnect is a standards based document that references 17 IETF documents as compared to the ATIS document that references 18 IETF documents, Consequently if the ATIS document is a Standards based document, then SIPConnect is also a Standards based document. Rejecting SIPConnect on the basis of being a manufacturers dominated document or Non Standards based document, without reviewing the value of SIPConnect does not help the NTWG. |
| 27 | 17May05 | F. Menard stated that the ability to move forward for Xit is limited by the unavailability of the description of the CCS7 Minimum Message Set, including TCAP. |
| 28 | 17May05 | The Chair renewed his invitation to the ILECS to document the CCS7 messages flow in the Minimum Message Set. |
| 29 | 17May05 | K. Richardson stated that he had been working on a contribution that would clarify the services supported by the Minimum Message Set described in TIRE009. R. Sired and H. Yabar volunteered to cooperate. |
| 30 | 21Jun05 | The TIF was approved as amended. |
| 31 | 21Jun05 | F. Menard reported that a working group within the SIP Forum is in a process of being chartered and will start work on July 6. The purpose of this working group is to define IP/Centrex intercarrier interoperability and SIP intercarrier interconnection |
| 32 | 21Jun05 | K. Richardson presented his contribution NTCO0324. The Chair thanked K. Richardson for his contribution providing such a comprehensive history H. Charles also considered K. Richardson’s contribution very appropriate and useful, and proposed to use it to get on with the task. F. Menard also thanked K. Richardson for his contribution. F. Menard also expressed that CCS7 message sequence charts are still missing. H. Charles stated that he sees that as the next step. K. Richarson stated that the ANSI and Bellcore documents are available for review. K. Richardson reminded that TELUS offered to provide the documents required to continue the work. Sam Yung clarified that TELUS has a technical library but not offered to provide the documents. TELUS will make the documents available through contributions. The Chair asked D. Kwong and R. Sired if they can provide the info required. F. Menard asked if CNAM was the only instance where TCAP messages are required in the MMS. K. Richardson responded that MMS requires TCAP also for Call Management Services. It was clarified that CNAM TCAP messages under bi-lateral agreement are part of the MMS. |
| 33 | 21Jun05 | H. Charles stated that a flow chart of SS7 messages could be developed in order to identify the corresponding SIP messages. H. Charles asked Bell Canada and MTS Allstream why is it so complicated to illustrate SS7 call flows.MTS Allstream responded that all the messages required for SS7 are detailed in the documents listed by K. Richarson. K. Richardson stated that if we looked at SIP Connect we would find an example of mapping SIP messages to CCS7 messages. |
| 34 | 21Jun05 | M. Segal stated that SIP has most of this messages already defined and why do we spend so much time discerning where to start. |
| 35 | 21Jun05 | H. Yabar presented NTCO0325. F. Menard committed to provide comments to MTS Allstream contribution by next meeting. |
| 36 | 21Jun05 | Videotron stated that they will provide their comments to Allstream contribution after the next meeting. |
| 37 | 19Jul05 | The TIF was reviewed and approved as amended. |
| 38 | 19Jul05 | Videotron stated that we need to specify the emerging technical standards currently being worked on to implement in IP the CCS7 Minimum Message Set (MMS). Videotron suggested to enquire vendors/manufacturers what features of the CCS7 MMS are they implanting on IP and what emerging technical standards are they using to do so. |
| 39 | 19Jul05 | Cogeco stated that identifying protocols that will support all the features is required |
| 40 | 19Jul05 | Consensus was reached to follow Keith Richardson’s proposal, based on his contribution NTCO324, that the members deconstruct the SS7 MMS and map each feature into its SIP equivalent message. Following is the list of members that volunteered to perform this task, with the commitment to provide their corresponding contributions for the upcoming meeting on September 13, 2005, when if they did not present their contribution, they commit to report on the status of it: Bell Canada - Basic SS7 Call Control as specified in TICO128a and based on the message sets ANSI T1.111 (192) Message Transfer Part, and ANSI T1.113 (1992) ISDN User Part. MTS Allstream – Calling Line Identification Presentation and Restriction Services as specified in TICO135 with the format and permissible field values of the Calling Party Number as specified in Chapter 3 of ANSI T1.113 (1992) ISDN User Part. TELUS – Call Forward Services as specified in TICO 136 according to the formats and procedures of Section 7 of ANSI Standard T1.611-1991, Supplementary Services for non-ISDN Subscribers. CCTA – Call Management Services as specified in TICO 118A according to the service descriptions and protocol specifications for the call management features in Bellcore technical references: CLASS Feature: Automatic Callback – TR-NWT-00215 Issue 2 March 1991, CLASS Feature: Automatic Recall – TR-NWT-000227 Issue 2 March 1991, and CLASS Feature: Screening List Editing – TR-NWT-000220 Issue 2 March 1991. Rogers – Calling Name as specified in TICO 199c according to ANSI T1.641-Calling Name Identification Presentation and ANSI T1.639-Calling Name Identification Restriction to support the ISUP and TCAP methods. |
| 41 | 19Jul05 | Doug Kwong committed to send an e-mail with the new link to PTSC-SAC. |
| 42 | 13Sep05 | The TIF was approved as amended. |
| 43 | 13Sep05 | H. Yabar presented NTCO0331. Doug Kwong presented NTCO0333. Doug Kwon committed resubmit his contribution providing a lay-out the SIP messages corresponding to figures 3, 4 and 6. James Chin presented NTCO0334. |
| 44 | 13Sep05 | CCTA reported that their contribution is progress and that it will soon be issued. |
| 45 | 13Sep05 | MTS Allstream, Cogeco and Bell Canada volunteered as editor of the report on IP-to-IP interconnection interface guidelines. The Chair offered to help with the preparation of the report. |
| 46 | 13Sep05 | NTCO0332 was not reviewed due to the absence of Xit Telecom’s representative. |
| 47 | 13Sep05 | The contributions were discussed in a lengthy detail and it was established that options exist to transmit information in SIP messages but not one common option was defined. The concept of Trusted Networks was also discussed in the context of SIP. |
| 48 | 19Oct05 | The TIF was approved as amended. |
| 49 | 19Oct05 | With respect to item 41, D. Kwong stated that he will not provide the new link to PTSC-SAC. |
| 50 | 19Oct05 | K. Richardson noted that the resubmission of NTCO0333 by D. Kwong, providing a lay-out of the SIP messages corresponding to figures 3, 4 and 6 is still outstanding. |
| 51 | 19Oct05 | Cogeco presented its contribution NTCO0336, showing the nature of SIP, that provides more than one option to accomplish the same objective. Specifically, Cogeco’s contribution showed the Packetcable and the Sipping approaches (both using SIP) for AR. The parties agreed to cogeco’s proposal to acknowledge that SIP provides the means to accomplish the equivalent of the TDM MMS. NTWG has not investigated other protocols. Xit Telecom asked why LNP is not part of the MMS. Xit believes that LNP can be provided by DNS in an IP environment. Videotron believes that LRN should be part of the parameters considered in the interconnection profile. But Videotron does not support the discussion of the TCAP query within the scope of this TIF. LNP was not discussed in any further detail |
| 52 | 19Oct05 | Xit Telecom presented its contribution NTCO0332. Xit telecom stated that authentication can use Transport Layer Security (TLS) between two proxy servers. Cogeco stated that ENUM discussions should be deferred until the CSCN publishes some resolution. Xit Telecom stated that an IP-to-IP interface should not include TDM for the resolution of LNP. Xit Telecom stated that IP-to-IP interface should contemplate ENUM for LNP resolution. Videotron stated that LNP is not in the scope of this TIF. Rogers asked if the Commission Regulates on how to obtain the LRN. Xit Telecom stated that the Commission regulated the establishment of the CLNPC. The Commission staff clarified that the Commission does not expect resolution or recommendation resolving LNP Herb Charles stated that the development of IP-to-IP NNI interface guidelines should be viewed as a work in progress, with the initial objective being to address the Minimum Message Set. Herb agreed with the Cogeco position that, in the context of MMS requirements across an NNI, a DNS query was irrelevant. Nevertheless, such related matters should be “parked” for possible future examination. The Chair proposed to include RTP and RTCP on the list of pending issues for an IP-to-IP interconnection. |
| 53 | 19Oct05 | Cogeco presented its contribution NTCO0335. Xit Telecom asked if Call Management Server to Call Management Server signalling standard (CMSS) was submitted to the ITU-T. The Chair asked for a substantiation of the relevance of the Standard Writing body that Cogeco feels it should be considered. |
| 54 | 19Oct05 | MTS Allstream contribution was deferred for the next meeting. |
| 55 | 19Oct05 | NTRE035 Draft Report on IP Interconnection Profile for Interconnection between service providers under the jurisdiction of the CRTC was presented by D. Kwong. It was agreed to add Call Management Services to the list on the Scope section as per NTCO324. The Chair committed to provide a paragraph for the Scope section stating that modifications to the existing regime were considered out of the scope of this TIF. Agreement was reached to modify the Figure 1: Scope of the Report, to reflect the Network to Network Interface as currently shown. It was agreed that SIP provides more than one way to transmit the required feature information. It was agreed that a SIP default arrangement has not yet been defined. It was discussed whether to issue two separate reports to the Commission or to issue one report addressing both. The initial preference seems to be issuing one report addressing both: - IP-to-IP interconnection interface guidelines, along with - A report detailing its progress as well as any outstanding issues. Some parties suggested adding a section: Recommendations for the outstanding issues. H. Yabar invited to all parties and particularly to the volunteering editors Cogeco, Bell Canada and TELUS to provide their input as soon as possible, so the document could be updated and timely distributed. |
| 55 | 02Nov05 | The Chair proposed to defer the approval of the TIF minutes to the 14-15Nov05 meeting given that some participants did not have the opportunity to read them yet. |
| 56 | 02Nov05 | The Draft Consensus Report was discussed. The Chair informed that the paragraph for the scope section of the NTRE0335 will be provided shortly. Cogeco committed to provide a list of outstanding issues to be included in the NTRE0335. H. Charles stated that the TIF report does not seem to address the Commission’s request: IP-to-IP interconnection interface guidelines… and that there are no apparent guidelines. It was agreed to specify in the body of the report that this is a Progress report on NTTF014. H. Yabar again invited to all parties and particularly to the volunteering editors Cogeco, Bell Canada and TELUS to provide their input as soon as possible, so the document could be updated and timely distributed. |
| 57 | 14Nov05 | The TIF was approved as amended. |
| 58 | 14Nov05 | MTS Allstream presented its contribution NTCO0341, concluding that a single interconnection, used for IP-to-IP peering between LECs, can also be used for the exchange of VoIP traffic between these LECs. Consequently, one common interconnection suffices for the exchange of all the IP traffic between two LECs, including VoIP. Bell Canada commented that all three diagrams present the same thing with two routers interconnected via IP. Bell Canada does not see the relevance of this contribution. Videotron stated that if we want to link the architecture to the guidelines, the signalling, voice bearer and security, among others should be considered. |
| 59 | 14Nov05 | The NTWG focused on drafting NTRE035, based on the second draft that was updated and distributed. |
| 60 | 06Dec05 | Given that the minutes were late and some participants did not have the opportunity to read them, the Chair proposed to defer the approval of the TIF minutes to the 10Jan06 meeting and the motion was adopted.. |
| 61 | 06Dec05 | H. Yabar read the recommendations section on NTRE035B and asked for comments and contributions. H. Yabar also stated that during the discussion of NTRE035B it was agreed that the NTWG should provide a list of issues that require the Commission’s guidance, together with a substantiation of the significance to the NTWG, for each item for which Commisssion’s guidance is requested. J. Ndirangu concurred. |
| 62 | 06Dec05 | Given that Cogeco sent a letter for the 14Nov05 meeting that was not discussed at that time due to the absence of the author, a contribution number (NTCO344) was assigned to it by the Chair, and Cogeco presented it stating that it was intended to be a starting point for discussion. |
| 63 | 06Dec05 | The Chair’s proposal to group the NTWG further activities was adopted, as follows: Issues that require Commission’s guidance Issues that the NTWG agrees to investigate further as part of NTTF014 Issues that can be parked for later consideration |
| 64 | 06Dec05 | In regard to clarifying what defines a service provider under the CRTC jurisdiction, Keith Richardson (RTS) expressed doubt that the question, as stated, would produce a response that is relevant for NTWG to further develop the NNI. Keith argued that the NNI should be the same whether the service provider is a CLEC, IXC or a Reseller. David McKeown (Shaw) commented that the question and the response from the Commission may provide indications that NTWG can use to develop practical interconnection guidelines that address the notion of “trusted network”. David further illustrated his view by citing that interconnection in the LD regime was allowed to Resellers and LD Carriers whereas in the Local service only Carriers were allowed to interconnect (CLECs and WSPs). Then David formulated the question as “whether interconnection would be allowed only to IP based carriers, or IP based carriers and resellers”. Similarly, Bell Canada formulated the question whether is it distinguishable between LD and Local carriers. David asked about the possibility of the industry conducting a simple IP-to-IP trial for the purpose of identifying and understanding relevant issues. |
| 65 | 06Dec05 | After ample discussion, the issues listed in NTCO344 were grouped as follows: Commission Guidance Clarifying what defines a service provider Interconnection architecture Number of POIs Demarcation Points Local transiting arrangements Toll interconnection EAS 2. NTWG agrees to investigate further as part of NTTF014 Verifying whether SIP is the best or not Clarifying whether lower layer protocols should be examined Signalling encryption and quality of service (QoS) Bearer traffic encryption and QoS, Codecs, Echo control LNP Privacy Relevant standards developing bodies Physical interconnection points and characteristics 3. Parking Lot Interface speed VLAN/VPN Transition consideration |
| 66 | 06Dec05 | The Chair invited all parties to present their contributions |
| 67 | 10Jan06 | Minutes of the last two meeting TIF notes were revised. NTTF14K TIF notes were approved. Changes to NTTF14L were suggested. Final approval is pending. Herb Charles asked the rationale of serial 65, since NTWG should be focusing on the interconnection parameters details instead of focusing on things that do not seem to be part of the scope of this TIF. Shaw explained briefly the rationale, by explaining the fact that it was an interrogation we had during the last meeting. Herb Charles argued that we should concentrate on defining an NNI FCI argued that a default set of definitive parameters should be agreed and part of the NNI. In fact it should be clear what should be done in order for interconnection to happen without any dispute. Cogeco replicated by proposing that a default set of parameters be define in order of having a dispute resolution mechanism. This reflects VoIP reality which supports a certain number of existing signaling standards or pre-standards. It might be indeed difficult choosing a default one. Xit indicated a preference for a completely predefined set of interconnection parameters. (Chair) Telus asked the question if we should then return to the commission for guidance as previously agreed. Herb Charles commented that we should stick to the technicalities. Shaw insisted that we need to have policy guidances. FCI insisted that we need to define the technicalities. Cogeco insisted on having guidance from the commission. (Chair) Telus commented that by not asking the question related to who should interconnect, and asking the fact that the actual interconnection architecture is adequate for IP-to-IP,, the NTWG would define technically and the commission should decide, what is left, by itself. Rogers argued that the CRTC would have to address both. While Bell Canada commented that we should stay on what is technical. (Chair) Telus asked the question if we should then look at redefining the LIR. Bell Canada asked why we would have to clarify. Shaw argued that technical interconnections details are important, but interconnection location is important as well. Videotron suggested a step by step approach which was supported by Cogeco. RTS suggested that ATIS would be a good technical approach. Herbs Charles responded that we would need to see the standard in order to agree. Same comment from Shaw who cannot agree that it is the best approach until the standard is available. Cogeco reinforced Shaw point. However Shaw, and Videotron agreed to take a look at Atis, if they can get a copy of the standard. RTS then suggested that the group should do a formal request to ATIS I order of getting a free version of their IP interconnection standard. Cogeco suggested that a letter be sent to the commission asking their guidance on the question related to NTWG defining point 1 of serial 65. There was no general agreement that a letter should be sent to the CRTC, even if the report highlighted that commission guidance will be requested. However RTS asked the question what to do if we need, like stated in the report, to ask the commission for guidance? Shaw proposed a possible contribution. Herb Charles proposed to write a draft letter for next meeting. (Chair) Telus asked NTWG member what should be the logical next step? Videotron suggested that point 2 of serial 65 should be a good start. Cable Companies present agreed to review NTCO307 and 308 and ATIS,IP interconnection standard assuming that the documentation is available. All present non-cable company members should review NTCO335 in order of understanding Packetcable input. |

ACTION REGISTER:

|  | Action | Opened | Prime | P Date | A Date | Status |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | To include a Background section in the TIF | 9Nov04 | H.Yabar | 07Dec04 | 07Dec04 | Completed |
| 02 | Present a revised work plan. | 15Feb05 | H.Yabar | 15Mar05 | 15Mar05 | Closed |

ASSSOCIATED CONTRIBUTIONS:

| Date | Contributor | Title | File ID | Reviewed |
| --- | --- | --- | --- | --- |
| 09Feb05 | Xit Telecom | SIPconnect Interface Specification v1.0 | NTCO297.doc | Yes |
| 22 Feb05 | Herb R. Charles | IP-to-IP Interconnection Guidelines | NTCO302.doc | Yes |
| 09Mar05 | TELUS | IP Protocol Evaluation | NTCO304 | Yes |
| March 05 | Bell Canada | IP to IP Carrier Interconnection | NTCO305 | Yes |
| 13Apr05 | K. Richardson | The Scope of NTTF014 | NTCO307 | Yes |
| 13Apr05 | K. Richardson | ATIS IP-IP Interconnection Protocol | NTCO308 | Yes |
| 10Jun05 | K. Richardson | The Minimum Message Set for IP-IP Interconnection | NTCO324 | Yes |
| 14Jun05 | MTS Allstream | Outline of Report on IP-to-IP Interconnection Interface Guidelines | NTCO325 | Yes |
| 13Sep05 | MTS Allstream | SIP Equivalent for Calling Line Identification Presentation and Restriction Services, as specified in TICO135 with the format and permissible field values of the Calling Party Number as specified in Chapter 3 of ANSI T1.113 (1992) ISDN User Part. | NTCO0331 | Yes |
| 08Sep05 | Xit Telecom | IP to IP Interface Interconnection Guidelines Draft Report & Proposal to create a separate document entitled: Progress Report identifying remaining outstanding issues. | NTCO0332 | Yes |
| 09Sep05 | Bell Canada | Typical Call Flow using SIP for VoIP at the NNI | NTCO0333 | Yes |
| 09Sep05 | Rogers Telecom Inc. | Calling Name mapping for IP to IP Interface Proposal | NTCO0334 | Yes |
| 05Oct05 | COGECO CABLE INC. | Proposed enhancements to Standards Writing Organizations (SWO) examples, based on the definition proposed in Telecom Order 98-40 | NTCO0335 | Yes |
| 11Sep05 | COGECO CABLE INC. | Proposed examples of SIP Call Management messages as a basis of comparison for the CCS7 minimum required message set. | NTCO0336 | Yes |
| 13Oct05 | MTS Allstream | LECs IP-to-IP Interconnection Scenarios | NTCO0341 | Yes |
| 14 Nov05 | COGECO CABLE INC. | COGECO’s proposed Further Activities section for NTWG Report NTRE0035 | NT CO0344 | Yes |

REPORT REGISTER:

| Report # | Title | File ID | Date of WG Approval | Date of SC Approval | Date of Commission Approval |
| --- | --- | --- | --- | --- | --- |

BACKGROUND:

From Previous CISC Meetings Minutes

CISC NTWG Meeting Summary - February 24, 2004

#### Proposed TIF – Session Initiation Protocol Profile for Interconnection Between Canadian Carriers

The NTWG reviewed the proposed TIF.  The following comments were made.

There are many protocols in the IP environment; it is premature to develop an interconnection profile based on SIP.

IP standards are evolving.  There is not enough knowledge on SIP to start working on an interconnection profile.  An industry scan of alternative standards is needed.

Not all IETF RFCs become standards even in the IP environment.

Not comfortable that the specifications such as IETF RFC and Packet Cable specifications are from recognized standards writing bodies, e.g., ANSI.

  - The NTWG needs an understanding about where the industry regulation is leaning before meaningful works can be done.  Lots of groundwork needed before an interconnection profile can be developed.

  - The Commission staff indicated that at the moment interconnection framework does not include IP interconnections although this does not prevent carriers from entering into bi-lateral agreement arrangements.  However, carriers are required to comply with the “no undue preference” rule and offer the same arrangement to other carriers.

In order to enable meaningful discussions and focus activities, participants are invited to submit contributions to better define / refine the scope of the proposed TIF for the next meeting.  Specifically, contributions should focus on the following:

Whether the WG can undertake the proposed task in whole or in parts?

If the proposed task needs to be modified, what should be in-scope and what should be out-of-scope?

Given this activity will only facilitate the development of bi-lateral arrangements and not an interconnection mandate, participants are requested to express their interest in participating in the task.

CISC NTWG Meeting Summary - April 06, 2004

#### Proposed TIF – Session Initiation Protocol Profile for Interconnection Between Canadian Carriers

Contributions were received from TELUS (NTCO289.doc), Xit Telecom (NTCO290.doc) and Bell Canada (NTCO291.doc).  The Bell contribution was distributed late, therefore in accordance to the CISC administrative guideline, presentation and discussion was postponed to the next meeting.

TELUS presented its contribution NTCO289.doc and answered questions from the WG seeking clarification of the contribution.

Xit telecom presented its contribution NTCO290.doc and answered questions from the WG seeking clarification of the contribution.

Discussion regarding the scope of the proposed TIF was postponed to the next meeting.

Francois Menard (Xit telecom) presented materials from several Internet resources on IP protocols.  Instead of assigning contribution numbers to the materials from the Internet and posting them to the CRTC web site, his email request was converted into a contribution (NTCO292.doc) and will be posted.

During the discussion, Louis LePage (CRTC) made reference to a presentation on VoIP standards that was given at the Telecommunications Standards Advisory Council of Canada (“TSACC”) meeting in March.  NTWG members can view this presentation at the TSACC web page http://www.tsacc.ic.gc.ca/e/.  (Note:  please follow the URL, login at the member section and then following the meeting documents folder.  You may be required to register before you can view this document.)

CISC NTWG Meeting Summary - May 11, 2004

#### Proposed TIF – Session Initiation Protocol Profile for Interconnection Between Canadian Carriers

Bell presented its contribution NTCO291.doc and answered questions from the WG seeking clarification of the contribution.

The Chair indicated that the WG should decide whether to approve the proposed TIF at the next meeting.

CISC NTWG Meeting Summary - June 15, 2004

#### Proposed TIF – Session Initiation Protocol Profile for Interconnection Between Canadian Carriers

Members generally supported the undertaking of a TIF to work on IP interconnection profile.  However, there was still a diverse view in regards to the scope of the TIF.

The Chair indicated that one final round of contribution will be accepted.  Contributions are due by next meeting.  Decision regarding the scope of the TIF was held over till the additional contributions are reviewed.

CISC NTWG Meeting Summary - July 13, 2004

#### Proposed TIF – IP Interconnection Profile for Interconnection Between Canadian Carriers

Despite the diverse views expressed at the June meeting and the extension for contributions, no additional contribution was received.

The WG members approved the creation of a new TIF –NTTF014, IP Interconnection Profile for Interconnection Between Canadian Carriers.  Henry Yabar of MTS Allstream volunteered to be the TIF owner.

The TIF will be submitted to the Steering Committee for approval.  The next Steering Committee meeting is scheduled for September, 2004.

CISC NTWG Meeting Summary - September 14, 2004

#### Proposed TIF – IP Interconnection Profile for Interconnection Between Service Providers Under the Jurisdiction of the CRTC

The proposed TIF was reviewed.  Following is a summary of the discussions and the agreements reached.

TIF title:  Some parties raised the concern that the term “Canadian Carriers” would restrict the applicability of the guideline to LECs within Canada while other parties contended that the mandate of CISC should remain focused on interconnection between carriers.  The Chair reminded members that the Commission would ultimately have to decide who could interconnect as peers and that NTWG should focus on developing a technical guideline that would be used for interconnection.  After much discussion, members agreed to replace “Canadian Carriers” with “Service Providers Under the Jurisdiction of the CRTC”.

Task Description:  The task description was revised from

The objective of this TIF is to develop an IP-to-IP interconnection interface guideline (reference document) that will assist Canadian carriers who are interested in interconnecting by natively exchanging VoIP traffic between themselves.

to

To develop an IP-to-IP interconnection interface guideline initially for telephony service providers that are under the jurisdiction of the CRTC.

Herb Charles objected to the term “telephony”, arguing that it would limit the task to voice application only.  Some parties argued that the phrase “… initially for telephony service providers …” provided the initial focus critical for the task.  Herb Charles agreed to accept the text so long as his objection is noted in the minutes.

Editorial changes were also made to the “Work Plan and Time Frames” section of the TIF.

The TIF will be submitted to the Steering Committee for approval.

CISC NTWG Meeting Summary - October 12, 2004

#### Proposed TIF – IP Interconnection Profile for Interconnection Between Service Providers Under the Jurisdiction of the CRTC

Sam Yung indicated that the finalized proposed TIF was submitted to the Steering Committee for approval at the October 15 meeting.

Note:  The proposed TIF was accepted by the Steering Committee at their October 15 meeting.

ASSSOCIATED BACKGROUND CONTRIBUTIONS:

| Date | Contributor | Title | File ID | Reviewed |
| --- | --- | --- | --- | --- |
| 12Sep2003 | Xit Telecom | Session Initiation Protocol (SIP) Profile for interconnection between Canadian carriers |  | Yes |
| 06Apr2004 | TELUS | Scope of a Proposed SIP Interconnection Profile Task | NTCO289 | Yes |
| 06Apr2004 | Xit Telecom | Scope of a Proposed SIP Interconnection Profile Task | NTCO290 | Yes |
| 07Apr2004 | Bell Canada | Comments on Proposed TIF re: SIP | NTCO291 | Yes |
| 31Mar2004 | Xit Telecom | PacketCable(tm) Call Management Server Signaling Specification PacketCable(tm) Interdomain Quality of Service Specification IETF Session Initiation Protocol Standards Track Request For Comment | NTCO292 | No |

# Comments

Telus asked to reword in a way of expressing that the TIF notes were late. Up to you Henry to decide what to do with it.

Comment from Telus: Please clarify phrases. Suggestion from Telus: Divide paragraph in two.